Magnum Motorsports, Ltd.

Setup Guide for N2K3

First off we here break the corner down into 5 zones

ENRTY ZONE / CUT ZONE / MIDDLE / ACCELERATION ZONE / EXIT

The ENTRY is basically the place the car is setting itself for the corner

The CUT ZONE is where you are actually entering the corner

The MIDDLE is fairly obvious

The ACCELERATION ZONE is where you are back on the gas or in most cases where you would like to be back on the gas

The EXIT is where you are for the most part out of the corner and transitioning onto the straightaway

See picture on last page

LOOSE ENTRY / CUT ZONE

Stiffer right front spring   (in turn will create more R/F tire wear and temp)

Less left rear sway bar    (will tighten the entry / cut zone and loosen car under acceleration)

More front weight              (in turn will create more R/F tire wear and temp)

Stiffer front sway bar        (will tighten the car on both entry and the exit)

Stiffer right rear spring    (will tighten the entry / cut zone and loosen car under acceleration)

Less right front neg. camber   (will tighten entry and exit)

More toe out

More front shock compression

Less rear shock rebound

More R/F caster

TIGHT CUT ZONE

Softer right front spring      (less R/F tire temp=less wear slight tighter exit)

Higher left rear track bar     (slightly less tire temp tighter exit)

Stiffer L/F spring                  (looser entry tighter exit)

Lower R/R track bar             (looser entry tighter exit)

Less front weight

Less L/F caster

Less R/F compression

More L/R rebound

TIGHT MIDDLE

Raise rear track bars   (usually evenly= looser thru out the corner)

Softer R/F spring         (nothing drastic here may make car to loose on entry)

Stiffer L/F spring          (looser entry middle/ tighter exit)

Stiffer R/R spring         (tighter entry/ looser middle out)

More caster split

Stiffer L/R rebound

Softer R/F compression

Less rear weight       (less weight on R/F front tire= less tire temp looser thru out corner)

More rear sway bar      (Seems to be creating more R/F tire temp though)

Less front sway bar     (mostly noticed in entry and exit)

LOOSE MIDDLE

Lower track bars        (usually evenly, will be felt thru out the corner)

Stiffer R/F spring        (more R/F tire temp/works mostly on 2nd ½ of corner)

Softer R/R spring        (less R/R tire temp works mostly on 1st ½ of corner)

Less L/R rebound

More R/F compression

Less rear sway bar

TIGHT ACCELERATION ZONE

Higher R/R track bar         (tighter entry looser exit)

Lower L/R track Bar          (tighter entry looser exit)

Stiffer R/R spring               (looser middle off)

Softer L/R spring               (looser middle off)

Less front weight

More L/F rebound

More R/F rebound

Less R/R compression

Less R/F compression

LOOSE ACCELERATION ZONE

Lower R/R track bar          (looser entry /tighter exit)

Raise L/R track bar           (looser entry tighter exit)

Softer R/F spring              (looser entry tighter exit)

Softer R/R spring              (tighter entry looser exit)

More front sway bar         (tightens entry and exit)

Less rear sway bar           (tightens car thru out corner)

More front weight

Less L/F rebound

LOOSE ACCELERATION ZONE continued

Less R/F rebound

Less R/R compression

TIGHT EXIT

Less L/R track bar                  (tighter entry looser off)

More R/R track bar                 (tighter entry looser off)

Stiffer R/R spring                    (tighter entry looser middle out)

Less front weight

Softer L/R spring                    (loosens car middle off)

More L/F rebound

More R/F rebound

More R/R compression

Less R/F compression

LOOSE EXIT

Softer R/R spring   (looser entry tighter exit / helps a lot with snap loose problems SNAP LOOSE the last second of the corner when u almost made it

And it stepped out

Less R/R track bar              (loosens entry tightens exit)

More L/R track Bar              (loosens entry tightens exit)

More front weight    (tightens car thru out corner /also big help in SNAP LOOSE

More front sway bar            (tightens entry and exit)

Less L/F rebound

More R/F rebound                (big help with SNAP LOOSE)

TIRES PRES ADJUSTMENTS

Right front

Higher psi     loosens EXIT

Lower psi      tightens thru out corner

Right rear

Higher psi     looser in tighter off

Lower psi      bit looser to start more tire temp =more wear

Left front

Higher psi     tighter entry and exit

Lower psi      looser off

Left rear

Higher psi     tighter middle off

Lower psi      looser middle out

TIRES PRES ADJUSTMENTS continued

1 pound of tire pressure equals 15 pnds of spring rate

TIRE PRESSURE “MATH”

This is the way to get your tire temps distributed evenly

Inside + the outside divided by 2 will tell you what the temp should be

1 pnd. Of tire pressure per deg (up or down)

256 + 250 = 553 divided by 2 = 253

Example

Inside         middle          outside

256	251             250                        middle temp should be 253

So this tire need 2pnds of air added

Thanks Rusty (Go4Broke)

BASIC SPRINGS

Right front

Stiffer      (tighter entry looser exit)

Softer      (looser entry tighter exit)

Right rear

Stiffer      (looser middle out)

Softer      (tighter middle out)

Left front

Stiffer      (tighter cut zone looser exit)

Softer      (looser cut zone tighter exit)

Left rear

Stiffer      (looser entry tighter exit)

Softer      (looser middle off)

Adjustment will in most cases have the opposite effect in the other end of the corner

(Looser exit generally means tighter entry)

Spring Dynamics

Softer L/F then R/F	creates a looser entry/tighter exit

Stiffer L/F then R/F	creates a tighter entry /looser exit

Softer L/R then R/R	creates tighter entry /looser exit

Stiffer R/R then LR	creates looser entry/tighter exit

SHOCKS

R/F

Higher compression	will tighten the car going into the corner

Lower compression             will loosen the car going into the corner

Higher rebound	will tighten the car coming out of the corner

Lower rebound	will loosen the car coming out of the corner

R/R

Higher compression	will loosen the car coming out of the corner

Lower compression	will tighten the car coming out of the corner

Higher rebound	will loosen the car going into the corner

Lower rebound	will tighten the car going into the corner

L/F

Higher compression	will tighten the car going into the corner

Lower compression 	will loosen the car going into the corner

Higher rebound	will tighten the car coming out of the corner

Lower rebound 	will loosen the car coming out of the corner

L/R

Higher compression	will loosen the car coming out of the corner     Lower compression	will tighten the car coming out of the corner

Higher rebound	will loosen the car going into the corner

Lower rebound                    will tighten the car going into the corner

Higher shock compression on the right side will help the car going into the corner                                                                                                             Lower compression in the rear shocks will loosen the car going into the corner                                                                                                                    Higher shock rebound on front shocks will help the car going into the corner (more to the rear)                                                                                           Lower  shock rebound on the front shocks will tighten the corner entry               (more to the front)

TOE OUT

More toe out creates more drag

Never less then 000

Never more then 0.125

More toe out tightens car thru out corner

RIDE HEIGHT

Higher L/F    (tightens car)

Higher L/R    (loosens car)

Higher R/R    tightens car)

CAMBER

More + R/F camber      (allows the car to turn in quicker & loosens the exit)         Less - R/F camber       (will make the car turn into the corner slower and tighten the exit)                                                                                                                     More + L/F camber      (and the car will turn in quicker & loosen the exit)            Less - L/F camber       (tightens the car in the middle of the corner & on exit)

WEIGHT

Front bias

More front bias makes the car tighter                                                                      Less front bias makes the car looser

WEDGE

+ or More wedge      (will tighten the car on entry and during                                                                                               corner acceleration)                                                                                                   - or Less wedge      (will make the car looser on corner entry and exit)

BREAK BIAS

+ More front brake       (higher % will tighten the car under braking)                         - More rear break         (less % will loosen the car during braking)